## Slide 1
SMART INDIA HACKATHON 2026
◦ PROBLEM STATEMENT ID - 26126
◦ PROBLEM STATEMENT TITLE - VISION BASED AUTONOMOUS NAVIGATION FOR UNMANNED GROUND VEHICLE FOR OUTDOOR ENVIRONMENT
◦ THEME - Smart Automation
◦ PS Category - Software
◦ Team ID - 137858
◦ TEAM NAME - HACKTIDE
Notes: Title slide. Backup problem statement for Team HACKTIDE (PS 26126, BEL).

## Slide 2
HACKTIDE
2
DRISHTI-Nav
See • Assess • Adapt — camera-only navigation that knows how much to trust its own eyes
One closed loop: perceive terrain, score risk and uncertainty, localise without GPS, replan on change, reach B safely.
END-TO-END AUTONOMY LOOP
1
Perceive
Lightweight segmentation labels grass, dirt, gravel, mud, rock, tree, ditch.
2
Assess
Energy score flags unknown pixels; a learned regressor rates frame confidence.
3
Localise
Visual odometry / SLAM + wheel odometry; tracking health monitored.
4
Map
Dynamic risk map 0–100 per cell: terrain, geometry, obstacle, unknown, staleness.
5
Plan
Global A* on risk cost fires on events; local arc planner at 10 Hz.
6
Move
Governor sets speed and margins from confidence; controller drives the UGV.
EXISTING APPROACH VS DRISHTI-NAV
Existing Approach
Binary free / blocked map
Shortest path at full speed
'Not detected' treated as safe
Blind to lighting changes
Full replan every frame
No measure of self-trust
→
DRISHTI-Nav
Continuous risk field (0–100)
Safer route, not just shorter
Unknown → uncertain → avoid
Confidence-aware speed & margin
Event-driven replanning
Localisation health → recovery
INNOVATION & UNIQUENESS
Multi-layer dynamic risk map
Terrain + geometry + obstacle + unknown fused per cell, updated every frame.
Unknown-aware perception
Energy-score OOD + 'novel' class: unfamiliar objects get risk, not a free pass.
Perception-confidence governor
Learned frame-quality score drives speed, safety margin and risk weight.
Event-driven replanning
Global A* only when the path corridor changes; local arcs at 10 Hz.
Lighting-adaptive behaviour
Shadows / low light → lower confidence → conservative navigation.
SAFETY BY DESIGN
Fail-safe autonomy
Every uncertainty has a response
Unseen cells carry risk, never 'free'
Hard stop on lethal cell ahead
Low confidence → slow + wide margin
SLAM lost → hold, re-acquire
Evidence accumulates, no phantom stops
Works with RGB-D / stereo, no GPS
Notes: Idea slide: the loop, the contrast with the standard camera->YOLO->SLAM->A* chain, the five innovations and the safety posture.

## Slide 3
HACKTIDE
FLOW AND ARCHITECTURE
3
1
UGV & sensors
Gazebo Harmonic outdoor world
RGB-D camera 640×480, 90° FOV
Wheel odometry — no GPS
Scenario runner: spawn obstacle, change sun
2
Perception with uncertainty
SegFormer-B0 / Fast-SCNN, 8 classes, ONNX
Energy score → per-pixel UNKNOWN
Frame confidence C (learned regressor)
CLAHE pre-processing when dark
3
Localisation
RTAB-Map RGB-D visual odometry
EKF fusion with wheel odometry
Tracking health H: features, inliers, lost
4
Risk map + events
Depth → points → 0.25 m cells; per cell: class belief, obstacle log-odds, height, unknown, confidence, last seen
risk = max(terrain, geometry, obstacle, unknown), pulled toward 'uncertain' when C is low; unseen = 35
Events: E1 new lethal cell on path · E2 corridor risk rise · E3 band change · E4 blocked > 2 s → replan
5
Behaviour governor
C, H → band NORMAL / CAUTIOUS / CONSERVATIVE / RECOVER
band → v_max, margin, risk weight λ, unknown weight
6
Adaptive planner
Global A* on 1 + λ·risk², events only (~30 ms)
Local: 52 arcs, 2 s rollout, 10 Hz
Shortest vs safest routes
7
Controller
Pure pursuit on local arc
Speed ≤ v_max(C)
Hard stop if lethal < 0.5 m
/cmd_vel → skid-steer
confidence C (from 2) + localisation health H (from 3)
λ, margin
v_max
/cmd_vel moves the UGV → new camera frame → loop repeats at 10 Hz
WHAT HAPPENS WHEN THE WORLD CHANGES
Rock appears 7 m ahead
detected in 1 frame → cell risk 92 → E1 → A* replan ≈ 30 ms → UGV passes with margin
Unfamiliar object
no class fits → energy score high → UNKNOWN → risk 60 + 50·u → treated as lethal, wider berth
Sun dims / shadows
confidence 0.95 → 0.47 → CONSERVATIVE: v 1.6 → 0.5 m/s, margin ×2, only risk < 66 driven
Light returns
confidence recovers → NORMAL band → speed resumes → Point B reached, zero collisions
PROTOTYPE VIDEO
Closed-loop simulation: risk map, unknown object, lighting event, replanning, A → B.
[YouTube link – add before submission]
Notes: Architecture: perception and localisation run in parallel and feed one risk map; the governor closes the loop from perception quality back into planning parameters.

## Slide 4
HACKTIDE
TECH STACK AND FEASIBILITY
4
TECHNOLOGIES USED
Simulation
ROS 2 Jazzy · Gazebo Harmonic · segmentation & RGB-D camera sensors · scenario runner (YAML)
Perception AI
PyTorch · SegFormer-B0 (3.7 M params) / Fast-SCNN · energy-score OOD · ONNX Runtime / TensorRT
Localisation
RTAB-Map (RGB-D) · robot_localization EKF · own ORB + PnP visual odometry as fallback
Planning & control
NumPy multi-layer risk map · A* (scikit-image / pyastar2d) · arc-sampling local planner · pure pursuit
Dashboard & eval
Foxglove Studio · FastAPI + WebSocket web view · seeded evaluation harness · CSV metrics
Proof-of-concept (now)
Pure Python: NumPy · SciPy · scikit-image · Matplotlib renderer · imageio (demo video, slide 6)
WHY THIS IS BUILDABLE BY A STUDENT TEAM
Simulator auto-labels every training frame → no manual annotation; RUGD / RELLIS-3D / ORFD for real-image fine-tuning.
Every module is NumPy-level maths on a 0.25 m grid; A* replans in ~30 ms, whole loop runs at 10 Hz on a laptop CPU.
Same ROS 2 nodes run on a Jetson with a RealSense / ZED camera — the simulator is swapped, not the code.
Working proof-of-concept already exists (video, slide 6): 45 seeded runs, 3 planner variants.
POTENTIAL CHALLENGES & RISKS
Textureless grass and sky make visual SLAM lose tracking outdoors.
Segmentation degrades under strong shadows, dusk and glare.
Objects never seen in training are misclassified as 'safe'.
Sim-to-real gap: simulator textures differ from real terrain.
ANALYSIS OF FEASIBILITY
All components are proven open-source parts (RTAB-Map, ROS 2, SegFormer) — the novelty is in how they are combined.
Risk table, bands and thresholds live in YAML — tunable without retraining.
Prototype loop runs 10 Hz on CPU; model is ~3.7 M params → embedded-ready (ONNX / TensorRT).
10-week plan: A→B with ground-truth pose by week 3, full stack by week 8.
STRATEGIES FOR OVERCOMING RISKS
● Fuse VO with wheel odometry (EKF); tracking-health signal → hold and re-acquire.
● Confidence governor slows and widens margins when lighting degrades; CLAHE pre-processing.
● Energy-score OOD + 'novel' class trained by outlier exposure in simulation → unknown gets risk.
● Domain randomisation (sun, textures, fog) + fine-tune on RUGD / RELLIS-3D real images.
Notes: Tech stack matches the earlier deck's structure: technologies, feasibility, risks, mitigations.

## Slide 5
HACKTIDE
IMPACT AND BENEFITS
5
IMPACT AREAS — what changes for outdoor UGV operations
GPS-denied defence mobility
UGVs keep moving under jamming, in forests, valleys and urban canyons where GNSS fails — BEL's core use case.
Search & rescue
Reaches casualties over rubble and unstable ground; unknown debris is avoided, not driven into.
Agriculture
Field robots choose firm ground over mud, cutting bogging and crop damage; runs on a low-cost camera.
Delivery, surveillance, mining
Perimeter patrol and last-mile logistics at dawn, dusk and under tree cover with adaptive caution.
KEY PROGRAM IMPACTS
Collision-free autonomy
0 collisions in 45 seeded runs; unknown objects and ditches avoided, not assumed safe.
Safer, not just shorter
Time in mud cut from ~40 s to under 1 s per run vs. binary planner; path ~13 % longer.
Self-aware perception
Confidence score tells the vehicle when to slow down — a first-class signal.
Fast reaction
New hazard detected within 1–2 frames, ~100–200 ms (binary map: ~960 ms); A* replan in under 30 ms.
Low cost, lightweight
One RGB-D camera, no LiDAR, no GPS; 3.7 M-param model runs on Jetson-class boards.
Measurable & reproducible
Seeded scenarios and ablations; every claim is a number from the harness.
TARGET AUDIENCE
1
BEL / defence UGV programmes
Camera-first autonomy module for GPS-denied outdoor platforms.
2
Disaster-response agencies (NDRF, SDRF)
Ground robots for reconnaissance over unstable terrain.
3
Agri-robotics & plantation operators
Low-cost navigation for field and orchard vehicles.
4
Logistics, mining & surveillance
Perimeter and last-mile autonomy in unstructured sites.
5
Robotics researchers & students
Open, simulator-agnostic reference stack with evaluation harness.
WHO GAINS WHAT
Operator
Vehicle reaches the objective without babysitting; risk appetite is one slider.
Platform maker
Drop-in software module; camera only, no GPS/LiDAR bill of materials.
Mission
Fewer stuck or damaged vehicles; predictable, explainable behaviour.
Right terrain · right speed · right margin — collision-free Point A → Point B without GPS
Notes: Impact slide structured like the earlier deck: impact areas, program impacts, target audience, who gains what.

## Slide 6
HACKTIDE
RESEARCH AND REFERENCES
6
PROJECT LINKS & DEMO
Proof-of-concept dashboard (t = 32 s): an unfamiliar object is flagged UNKNOWN (magenta) in the camera and the map; the risk-aware route (white) leaves the mud belt (orange) that the shortest route (grey) crosses; VO estimate vs ground truth, confidence gauge, governor band and event log.
PROTOTYPE RESULTS — 15 seeded runs per planner, same world
Metric | Binary planner | Risk-aware | DRISHTI-Nav
Success (no collision) | 100 % | 100 % | 100 %
Runs with collision | 0/15 | 0/15 | 0/15
Time driving in mud (s, mean) | 39.7 s | 1.6 s | 0.6 s
Hazard detection latency (ms) | 960 | 100 | 213
Global replans / run | 43.1 | 5.3 | 23.2
Path length (m) | 94.1 | 101.8 | 106.2
PROTOTYPE VIDEO
Full walkthrough of the working simulation (4 min) · [YouTube link – add before submission]
GIT-HUB LINK
Complete repository — simulator, perception, risk map, planner, dashboard, evaluation harness · [GitHub link – add before submission]
RESEARCH & REFERENCES
1. Wigness et al., RUGD: A Dataset for Autonomous Navigation in Unstructured Outdoor Environments, IROS 2019.
2. Jiang et al., RELLIS-3D Dataset: Data, Benchmarks and Analysis, arXiv:2011.12954 (2020).
3. Viswanath et al., OFFSEG: A Semantic Segmentation Framework for Off-Road Driving, 2021.
4. Guan et al., GANav: Efficient Terrain Segmentation for Robot Navigation, IEEE RA-L 2022.
5. Min et al., ORFD: A Dataset and Benchmark for Off-Road Freespace Detection (lighting/weather variation).
6. Liu et al., Energy-based Out-of-distribution Detection, NeurIPS 2020.
7. Hendrycks et al., Deep Anomaly Detection with Outlier Exposure, ICLR 2019.
8. Lakshminarayanan et al., Simple and Scalable Predictive Uncertainty via Deep Ensembles, NeurIPS 2017.
9. Frey et al., Fast Traversability Estimation for Wild Visual Navigation, RSS 2023; RoadRunner, ICRA 2024.
10. Campos et al., ORB-SLAM3, IEEE T-RO 2021; Labbé & Michaud, RTAB-Map, J. Field Robotics 2019.
11. Macenski et al., Nav2 — ROS 2 Navigation Stack; arXiv:2407.18535 (RGB-D → costmap layer).
12. Koenig & Likhachev, D* Lite, AAAI 2002; Fox et al., Dynamic Window Approach, 1997.
13. Xie et al., SegFormer, NeurIPS 2021; Poudel et al., Fast-SCNN, BMVC 2019.
14. BEL Problem Statement 26126, Smart India Hackathon 2026.
Notes: References mirror the literature review; video and GitHub links to be inserted by the team.